## Slide 1
Battery Management System

## Slide 2: Overview
Rahimieichi, H. , et al. "Battery Management System: An Overview of Its Application in the Smart Grid and Electric Vehicles." Electrets 2013.
Notes: Ensure safety.
Monitoring the condition of the battery.
Prolong the life of the battery.

## Slide 3: Important part: State Estimation
Problem: Battery Degradation
Estimate the state of charge (SOC), state of health (SOH), remaining useful life (RUL).
Prevent unpredictable failure.
Need a precise battery model.
Need a comprehensive definition of state of health.

## Slide 4: State Estimation Methods
Xuebing, et al. "A review on the key issues of the lithium ion battery degradation among the whole life cycle - ScienceDirect." eTransportation 1:100005-100005.

## Slide 5: Equivalent Circuit Model
R-2RC Model
R0 stands for resistance of contacts, electrodes, and electrolytes.
RCs simulate the dynamic features during charge and discharge.

## Slide 6: Simulink: Naive Version
I (t) > 0 : Discharge
I (t) < 0 : Charge
Nominal charge
Look-up table based on SOC & temperature

## Slide 7: Simulink: Result

## Slide 8: Data-driven methods
Mainly based on machine learning approaches.
Recent work mainly focused on CNNs or LSTMs.
Achieving really high accuracy in few steps ahead prediction.
Wang, C. , et al. "Dynamic Long Short-Term Memory Neural-Network- Based Indirect Remaining-Useful-Life Prognosis for Satellite Lithium-Ion Battery." Applied Sciences 8.11(2018):2078.
Notes: [1] Ardeshiri, R. R. , et al. "Machine Learning Approaches in Battery Management Systems: State of the Art: Remaining useful life and fault detection." 2020 2nd IEEE International Conference on Industrial Electronics for Sustainable Energy Systems (IESES) IEEE, 2020.

## Slide 9: Challenges
Model-based
  Different methods focus on different features of the battery.
  Too simple => Not able to capture the feature.
  Too complicate => Overfitting.
  Hysteresis effect.
Data-driven
  High cost to get run-to-failure data.
  Real environment will introduce noise.
  Need more accurate long-term prediction.
  High computation cost for online implementation.

## Slide 10
Thank you!